# Especificaciones Técnicas y Detalle de Precio

# Gateways – Equipos y Adicionales

- Objeto del requerimiento:

Con el fin de optimizar esquemas de redundancia para sistemas de telefonía IP existentes, economizar espacio en racks y consumo energético, permitiendo a su vez la migración gradual de centrales Legacy hacia una arquitectura NGN con equipamiento existente, ampliaciones paulatinas y unificar su servicio de telefonía privada, Centurylink Argentina lanza el siguiente concurso solicitando el equipamiento que se detalla a continuación.

- Cantidad de Unidades a adquirir:

| ITEM | DESCRIPCION | CANTIDAD |
| --- | --- | --- |
| 1 | VoIP Gateway Control Unit with 4 slots for VOIP, extension or trunk cards, with 2 Port Ethernet Switch (10/100Base-T), 1 Door Phone Entry Relay Port, 19” Rack Mountable, or wall mountable | 186 |
| 2 | Módulo de Expansión de 16 puertos Analógicos | 4 |
| 3 | Tarjeta interna de 8 puertos analógicos | 266 |
| 4 | Equipo de rackeo para VoIP Gateway Control Unit | 191 |
| 5 | Tarjeta Single de Troncal Digital E1R2 | 1 |
| 6 | Tarjeta Combo ATM con 4 puertos para líneas analógicas, 6 puertos para internos digitales y 2 puertos de extensiones analógicas | 186 |
| 7 | Tarjeta SD ALAW | 186 |
| 8 | Cable RJ45 de 3 metros de color rojo provistos por la misma marca | 744 |
| 9 | Módulos de compresión de voz hasta 32 canales | 1 |
| 10 | Módulo de Expansión de 30 puertos Analógicos | 1 |
| 11 | Tarjeta de 2 puertos analógicos | 27 |
| 12 | Tarjeta de 4 puertos de Troncal Analógico | 1 |

- Características Requeridas:

# 3.1 Especificaciones comunes a todos los equipos solicitados:

-Soporte de los siguientes features:

Media Gateway de Alta Capacidad

| Capabilities |
| --- |
| Capacity | 272 Extensiones analógica, 384 extensiones digitales, o 272 Extensiones IP (384 Extensiones Totales) Expandible sumando hasta 8 Expansión Módulos (Línea o Extensiones) Soporta: 2 T1 / PRI • Hasta 48 canales de datos Puerto de relé de entrada de teléfono de 1 puerta |
| Voice Coders | G.711 A-law/U-law. · G.723.1 MP-MLQ. · G.729 Annex A – CS-ACELP. |
| Fax Support | Fax/Modem Detection Control, T.38 (IP) compliant Group 3 fax relay |
| DTMF | Packet side or PSTN side detection and generation, RFC 2833 compliant |
| Voice over Packet Capabilities | H.323 V2 (1998), Packet-based multimedia communications systems. · Q.931, ISDN user-network interface layer 3 specification for basic call control. · H.225.0 (1998), Call signaling protocols and media stream packetization for packet-based multimedia communication systems. · H.245 (1998), Control protocol for multimedia communication. · Session Initiation Protocol. |
| Internet Standards/Specification (in addition to TCP/UDP/IP) | RFC 1889 – RTP/RTCP, Real Time and Real Time Control Protocol. · RFC 2507, 2508, 2509 – Header Compression. · RFC 2474 – DiffServ, Type of Service field configurable. · RFC 1990 - PPP Fragmentation. · RFC 1490 - Encapsulation for Frame Relay. · RFC 2686 - Multiclass Extensions to Multilink PPP. · RFC 3261 - Session Initiation Protocol (SIP). |

| Security | E911 • PIN-restricted terminals • CLI call-back for Remote Access • Integral Firewall • Network Address Translation (NAT) • PAP/CHAP authentication protocols • Time profiles • VPN support • System Management Audit Trail |
| --- | --- |
| Networking | Q.Sig Networking over T1 and IP • Uniform Dial Plan • Preferred Edition Networked Messaging • Proactive remote monitoring via SNMP • VPN support - IPSec or L2TP • SIP trunking to low-cost Internet Telephony Service Providers (ITSP) • Multi-site option (up to 32 sites) features such as Busy Lamp Field, Paging, Desk-to-desk calling, Calling/connected name and number, Hold and Transfer, Centralized Voicemail, Internal Directory, Absent Text Message, Anti-Tromboning, Remote Hot-Desking and Distributed Hunt Groups. |
| Data Functionality | Bandwidth on demand • DHCP server • Integral data router – RIP-2 • Internet Access • LAN-to-LAN routing • Multi-Link PPP • Remote Access Server (RAS) |

| Maintenance |
| --- |
| Management | Element Management System, SNMP v2 over IPSEC/SNMP v3, Command Line Interface (CLI) Must be managed by Avaya IP Office manager |
| Maintainability | All shelf modules are hot swappable, including boards, power supplies, fans |

| Hardware Specifications |
| --- |
| Interfaces | 2 IP Interface (LAN y WAN) Integral 10/100 Mbit Layer 2 Ethernet Switch Integral 10/100 Mbit Layer 3 Ethernet Switch |
| Unit Dimensions | 17.5 W x 2.9 H x 14.4” D (445 x 73 x 365mm); Minimum clearance front and back: 3” (75mm) |
| Operating Temperature | 32° to 104°F (0° to +40°C). 95% relative humidity, non-condensing |
| Power Supply | 100-240V AC, 50/60Hz, 81-115VA, 2.5A maximum |
| Cooling | Replaceable fan trays & filters |

Modulo de Expansion

| Capacity | 16 puertos o 30 puertos |
| --- | --- |
| Minimum Software Level | IP Office core software level 2.1(36) minimum. Bin file = dvpots.bin. |
| Included | Power supply unit and Expansion Interconnect cable. |
| Power Supply | The module is supplied with a Earthed 3-Pin, 60W external power supply unit. The PSU has an integral power cord for connection to the module's DC I/P socket |
| Mounting | The module is designed as a free-standing module that can be stacked on or under other IP Office modules. The module can be wall or rack mounted |
| Dimensions | Width: 445mm/17.5". Depth: 245mm/9.7". Height: 71mm/2.8". |
| Weight | Unboxed: 3.1Kg/6.94lbs. Boxed: 4.4Kg/9.7lbs |
| DC I/P | DC power input port. Used for connection of the power lead from an Avaya earthed 60W external power supply unit supplied with the expansion module |
| DTE | 9-Way D-Type socket |
| EXPANSION | RJ45 Socket. Used for direct connection to an Expansion port on an IP Office control unit using the Expansion Interconnect cable supplied with the module. |
| PHONE | RJ45 socket. Used for connection of analog phones. Intended for two-wire analog phones. For connection to 4-wire analog phones connection should be via a master socket with ringing capacitors. |

Analog Phone Base Card

| Capacity | 2 puertos o 8 puertos |
| --- | --- |
| Features | Supports ICLID modes DTMFA, DTMFC, DTMFD, FSK and UK20. · REN 2 (1 for external bell device). · Off-Hook current: 25mA · Ring Voltage: 40V. · Intended for connection to two-wire analog phones, the ports do not include a ringing capacitor. For connection to 4-wire analog phones, connection should be via a master socket with ringing capacitors. · If fitted with an analog trunk card, for the Phone 8, during power failure extension port 8 is connected to the analog trunk port 12. |
| Port LEDs | No status LEDs are used for analog phone extensions |
| IP500 Trunk Card Support | 1 |
| Maximum per Control Unit | 4 |

ATM Combination Base Card

| Capacity | 6 puertos digitales + 2 puertos analogicos + 4 puertos truncal analogico |
| --- | --- |
| Supports | 10 voice compression channels. Codec support is G.711, G729a and G.723 with 64ms echo cancellation. G.722 is supported by IP Office Release 8.0 and higher. |
| Power Failure | During power failure phone port 8 is connected to analog trunk port 12. |
| IP500 Trunk Card Support | 1 |
| Maximum per Control Unit | 2 |
| Minimum Software Level | 9.0 or Higher |

Tarjeta Single de Troncal Digital E1R2

| Capacity | Tarjeta de Troncalizacion E1 Single/Dual |
| --- | --- |
| Supports | Conexión para 1 E1 Configurado inicialmente para 8 canales en single. Requiere licencias para usar hasta 24 canales Tarjeta hija, requiere instalación de una tarjeta madre Máximo de 4 por equipo |
| IP500 Trunk Card Support | 1 |

Cable RJ45 de 3 metros de color rojo provistos por la misma marca

| Description | El cable Avaya RJ45 3M (RDSI rojo) es un cable RDSI de tres metros Par trenzado sin blindaje (UTP) Longitud: 10 pies Color rojo Conector: 1 x RJ-45 - Conector macho Otro lado: 1 x RJ-45 - macho Normas conformes: EIA / TIA-568 Categoría 5 Se requiere uno de estos para cada T1 / PRI o troncal analógico conectado a las tarjetas hijas internas Compatible con Avaya IP Office 500 V2 |
| --- | --- |

- Detalle del precio:

El oferente deberá completar la tabla de precios adjunta de acuerdo a las especificaciones técnicas y el objeto del pedido de cotización. Los precios serán fijos y no incluirán el IVA, sales taxes o similar.

| ITEM | DESCRIPCION | CANTIDAD | MONEDA | PRECIO | PRECIO | CONDICION |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | UNITARIO | TOTAL | INCOTERM |
| 1 | VoIP Gateway Control Unit with 4 slots for VOIP, extension or trunk cards, with 2 Port Ethernet Switch (10/100Base-T), 1 Door Phone Entry Relay Port, 19” Rack Mountable, or wall mountable | 186 |  |  |  |  |
| 2 | Módulo de Expansión de 16 puertos Analógicos | 4 |  |  |  |  |
| 3 | Tarjeta interna de 8 puertos analógicos | 266 |  |  |  |  |
| 4 | Equipo de rackeo para VoIP Gateway Control Unit | 191 |  |  |  |  |
| 5 | Tarjeta Single de Troncal Digital E1R2 | 1 |  |  |  |  |
| 6 | Tarjeta Combo ATM con 4 puertos para líneas analógicas, 6 puertos para internos digitales y 2 puertos de extensiones analógicas | 186 |  |  |  |  |
| 7 | Tarjeta SD ALAW | 186 |  |  |  |  |
| 8 | Cable RJ45 de 3 metros de color rojo provistos por la misma marca | 744 |  |  |  |  |
| 9 | Módulos de compresión de voz hasta 32 canales | 1 |  |  |  |  |
| 10 | Módulo de Expansión de 30 puertos Analógicos | 1 |  |  |  |  |
| 11 | Tarjeta de 2 puertos analógicos | 27 |  |  |  |  |
| 12 | Tarjeta de 4 puertos de Troncal Analógico | 1 |  |  |  |  |

- Homologación

Cualquier oferente que declare en forma explícita y fehaciente su compatibilidad total con el presente requerimiento y no sea hasta el momento proveedor de la empresa para tecnologías mencionadas y modelos ofrecidos, deberá atravesar un proceso de homologación interna para comprobar la compatibilidad de los equipos con el resto de la red.

- Tiempo de Entrega

El plazo de entrega del mismo (en la condición pactada de acuerdo al origen de la mercadería) deberá ser no mayor a 15 días a partir de generada la Orden de Compra. El cumplimiento de este plazo es un condicionante fundamental en la cotización.

- Nota de Compatibilidad

Todo el equipamiento suministrado debe ser compatible con los equipos Avaya IP Offices 500v2 Media Gateway y con Avaya Offices  Contact Center.